TCE tutorial:
From C to VHDL as quickly as possible
This tutorial shows how you can quickly turn your C code into parallel code and a VHDL-model of a processor using the TCE toolset
The basic idea is that you compile the C code, pass the sequential code to the design space explorer tool and let it generate a processor design capable of running the program for you
This tutorial has been tested with rev 3451 of TCE

---
Initial setup
Download and unpack the tutorial file package
  - wget http://tce.cs.tut.fi/tutorial_files/explorer_c2vhdl.tar.gz
  - tar -xvvzf explorer_c2vhdl.tar.gz
  - cd c2vhdl
There is an application directory which contains an example C source code, the “complex multiply” benchmark from DSPstone

---
Compile the sources
First compile the C sources of the programs into generic sequential TTA programs using the TCE frontend compiler
Note that the compiler output file must be named 'sequential_program'
  - gcc-tce -O2 -o application1/sequential_program application1/complex_multiply.c

---
InitialMachineExplorer:
Generating a Processor for the Program
First we use “initial machine explorer” to create an initial processor design capable of running the input program
  - explore -e InitialMachineExplorer -a application1/ -p build_idf=true ExplorerResults.dsdb
    - -e <plugin> specifies the plugin to be used in exploring
    - -a <dir> specifies an application searchpath to be added to the ExplorerResults database
    - -p option passes the parameter to the plugin - in this case the initial machine explorer plugin is instructed to also generate an implementation description of the processor design (not only an architecture description) so we can generate a VHDL implementation for it
    - Last parameter is the design space data base (DSDB) to store the explored processor configurations (architecture and implementation description file pairs) for later use
After running for a while, explorer should create a processor configuration to the DSDB with ID 1
  - This part of TCE is quite unoptimized so it can take several minutes to finish
  - To save time, ready-made results are included in 'ExplorerResultsPre.dsdb' which you can use instead of waiting to produce a new DSDB
  - The first configuration includes all the necessary resources but it is fully connected

---
SimpleICOptimizer:
Optimizing Connectivity of the Processor
Optimize the initial configuration using “simple IC optimizer” which removes unused connections from the processor
  - This phase can be skipped in case a fully connected machine is acceptable
  - explore -e SimpleICOptimizer -s 1 ExplorerResults.dsdb
    - -s <conf_ID> option defines the processor configuration to be optimized
A new processor configuration with a reduced connectivity processor architecture has been added to the database
  - Again, to save time, the resulting DSDB of this phase has been pregenerated to ExplorerResultsPre2.dsdb

---
Inspecting the Results
You can export the processor configurations from the database with:
  - explore -w <conf_ID> <database_file>
It will generate <ID>.adf and <ID>.idf files
  - ADF is the architecture description, and IDF describes which implementations to use for each architectural component
  - explore -w 1 ExplorerResults.dsdb # the configuration before connectivity reduction
  - explore -w 2 ExplorerResults.dsdb # the configuration after unused connectivity was removed
You can check how the architectures look like by running the Processor Designer GUI:
  - prode 1.adf & prode 2.adf &

---
...Inspecting the Results
If you want to get a (rough) estimate of the die area and the longest path delay of the processors you can run the Cost Estimator:
  - estimate 1.adf 1.idf
  - estimate 2.adf 2.idf
  - Again, this can take several minutes with the current unoptimized TCE code, so here is the output from the commands:
  - The longest path delay is 15 ns for both, which equals to about 67 MHz maximum clock rate
    - The longest path was not at IC, thus reducing IC didn't improve the speed
    - Area was reduced by 8.5% with the IC reduction
estimate 1.adf 1.idf
total area: 13324 gates
delay of the longest path: 15 ns
estimate 2.adf 2.idf
total area: 12181 gates
delay of the longest path: 15 ns

---
Generating Code for the Processor
Compile the sequential program for the generated architecture:
  - schedule -t 2.adf -o application1/parallel_program.tpef application1/sequential_program
Then generate encoding (a binary encoding map file, BEM) for the instructions:
  - (A bug workaround: add a read connection to 'boolean' RF with 'prode 2.adf&' before the next step! TODO: Remove this step from the tutorial after the bug has been fixed.)
  - createbem 2.adf
    - This creates 2.bem
Generate bit image of the instruction memory:
  - cd application1
  - generatebits -b ../2.bem -d -t parallel_program.tpef ../2.adf
This creates parallel_program.img and parallel_AS2.img into the application directory:
  - Contents of the program memory and the AS2 data address space, respectively in zeros and ones ascii format

---
Inspecting instruction encoding
You can examine the processor instruction encoding using BEM viewer:
  - viewbem 2.bem | less
  - BEM viewer outputs its results to terminal so it is useful to pipe the command with less or more
The most interesting number is the total instruction width
  - If you exported the non-optimized configuration from the database and created BEM for it, you can see that reducing connections decreases instruction width
Under the total instruction width is shown what instruction consists of
There is also a more detailed explanation for each move slot

---
Generate the processor implementation
Generate the processor VHDL implementation using Processor Generator:
  - generateprocessor -b 2.bem -i 2.idf 2.adf
Creates folder 'proge-output' which includes the VHDL files of the processor
  - Generating a test bench for the processor automatically is not yet supported, but will be in the future
  - Test bench will provide the memory components, initialization code, and clock generation code for testing the TTA code in a VHDL simulator easily
The processor implementation is now ready to be simulated in a VHDL simulator (if you provide a test bench!) and synthesized